## Slide 1: Presentation 1
Camilo Aguilar

## Slide 2
Short Term Goals:
  Understand Load Signatures.
  Signal decomposing and processing.
  Understanding hardware implementation and troubleshooting
Load Signatures
Hardware
Source: Surf PPT Presentation

## Slide 3: Load Signature
Electrical behavior
Understand and analyze:
  Control devices
  Energy Management

## Slide 4: Variables Load Signatures
Voltage (V)
Current (i)
Power (P)

## Slide 5: 1 appliance vs n appliances
Chart: Laptop (Time frame 0.020 s/100 data points)
Chart: FAN(time frame = 0.020 s/data points = 86 )

## Slide 6: Principle Superposition = Composite Load
Chart: Laptop + Fan

## Slide 7: Composite Load
  Unique features from appliances are mixed
  Certain features may be masked or lost. Decompose signals:
    Snapshot Form: Instantaneous snapshot of the load behavior taken at a fixed time intervals.
    Delta Form: Difference between two consecutive snapshots form signatures.

## Slide 8: Criteria to Classify Composite waveforms
    Current waveform
    Active and reactive power
    Harmonics
    Instantaneous Admittance Waveform
    Instantaneous Power Waveform
    Eigen Values

## Slide 9: Propositions
  Set a fix interval
  Normalize the data
  Set a threshold variation. (difference in voltage, power, current)
  Detect events by switching on/off appliances.
  By analyzing delta forms, and using an algorithm, extract feature changed.
  With a known database of features, match database with change in composite load signature.

## Slide 10: Eagle

## Slide 11: Long Term Goals
Implementing knowledge about load signature decomposition with hardware
Developing the program that will recognize each appliance