## Slide 1: Smart Power for the Smart Home: Inverter Controls, Power Factor Corrections, and Peak Demand Reductions
G.P. Li, Keyue Smedley - UC Irvine
California Plug Load Research Center
Power Electronics Laboratory
Mark Modera, Nelson Dichter - UC Davis
Western Cooling Efficiency Center

## Slide 2: Smart Load Management and Generation for Zero Net Energy Residences
Background:
  Capacitance and inductance create and consume reactive power
  Reactive power introduces difficulties maintaining a robust grid
  Not possible to charge consumer for reactive power
  Minimal consumer concern and resources allocated to correct and monitor the power factors
Project Goal:
  Enable smart management of electric loads and generation for zero net energy residences while advancing three technological elements

## Slide 3: Benefits for Utilities and Users
Current:
  ~30% of national electricity usage is for residential areas
  15.9GW of PV installed in US by Q2 2014
  Can power 3.2 million homes
Challenges:
  PV is an intermittent energy source
  Various plug loads cause power factor to fluctuate
Solution:
  Active power factor correction at PV inverter and home ADR

## Slide 4: Main Technology Advancements
Inverter-integrated active power factor correction
Load signature analysis for wireless load monitoring and control
Integrated design and control of HVAC and storage for shifting peak demand (UCD)

## Slide 5: Inverter-integrated active power factor correction
Typical PV inverter provides active power only
Reactive power from the load will be passed to the grid
In net-zero situation, pure reactive will go to grid
Active power filter can cancel the reactive power

## Slide 6: Active Power Filter Function
Remove reactive load and harmonic components
Realize power factor near 1
Reduce line losses
Increase line capacity
Protect sensitive loads
APF operation waveforms:
Grid voltage
Grid current
Load current
APF current

## Slide 7: APF Objectives
This phase
Implement 1.5kW APF
Test and fine tune in the lab
Real circuit demonstration
APF can be used for retrofit
Next phase
Inverter with APF function built-in will be pursued
Field demonstration of inverter under net zero condition will show zero reactive and harmonics

## Slide 8: Load signature analysis for wireless load monitoring-- Objectives
Background:
  Little to no incentive for end users to shift off peak hour consumption
  Consumer usage behavior information can be utilized to promote energy conservation
Objectives:
  Provide utility end-use information for billing, efficiency program marketing, or demand response control
  Provide load consumption feedback for users or for EMS

## Slide 9: Load signature analysis for wireless load monitoring -- Approach
Technical Approach:
  Use energy metering IC to measure real and reactive power to track and categorize appliances (macro load signature)
  Use first 15-second waveform to further identify devices (micro load signature)
  Use FFT to obtain harmonic content
  Match devices from a database of load signatures and usage patterns of the consumers

## Slide 10: Load signature analysis for wireless load monitoring – System Layout
Capturing Analysis  Display
Transient
FFT
Harmonic Features
Transient: PF, Power, Reactive Voltage and Current
Frequency: Harmonic Features
Load Characteristics
15sec
Steady
States
Signal comes in
Load Characteristics matching
Server
Mobile Interface
System Layout:
Capture (ADE7763) Analyze (ARM & Linux) Data Storing (Server) Display (HTML Mobile Interface)

## Slide 11: Load Signature Monitor and Report – Progress
Sectional Mobile Interface
Current and voltage probe measurements to build device library
Current Probe and TI2530 on SmartRF05 Board, with Raspberry Pi
ADE7763 to Arduino, to server
Capture and Analysis Progress

## Slide 12: UC Davis Field Demonstration
UC Davis will conduct field demonstrations at the Honda Smart Home in Davis, California.
APFC device developed by UC Irvine will be installed and monitored to assess:
  Energy flows and efficiencies for the device
  Power factor correction effectiveness
  Improvement to harmonics generated by the Smart Home
Load signature analysis device will be installed
  Functionality and user interface will be demonstrated

## Slide 13: UC Davis Modeling
UC Davis will use EnergyPlus to model a ZNE home
Simulations will include:
  Alternative mechanical system efficiencies
  Alternative load shifting strategies
  Different levels of generation
  and storage
  Differences in stochastic user behavior
  Differences in end use load profiles, including electric vehicle use
UC Davis will use MATLAB model of APFC device provided by UC Irvine to post-process EnergyPlus results
  Results will be used to determine impact of APFC device on the grid in various scenarios